## Slide 1: PV Forecast model
Flow Chart
Made by gyeong gak, Kim

## Slide 2
Data Foremat
Longterm data &
Forecast data
Month: 1~12
day: 1~31
Hour: 0~23 [h]
Quarter: 1~4 [0= 0 minute, 1= 15minute, 2= 30minute, 3= 45minute]
P1(humidity): 1~100 [%]
P2(Wind speed): 0~ [m/s]
P3(temperature): -~ [℃ ]
P4(Cloud Cover): 1~4 [1=sunny, 2=A little sunny, 3=a little cloudy, 4=cloudy]
P5(Rain)=0 ~ [mm]
P6(Solar Irradiation):0 ~ [MJ/]
Generation: [W],[kW],[MW]
Shortterm data

## Slide 3
Get File path
PVset_setPVModel
Longterm data
Set valid day/data
Devide data
Train Forecast Model
Validate model using valid data
Set coefficients each model using PSO
Intergrate individual model result
Calculate error
Build the error distribution
Save parameter
(.mat file)
Train data
Valid data
Vaild_predictors
Train ANN
(PVset_ANN_Train)
Train Kmeans
(PVset_Kmeans_Train)
Train LSTM
(PVset_LSTM_Train)
25x4
hour=1~25
Quarter=1~4
valid day=30
1x30
Forecast using ANN
PVset_ANN_Forecast
Forecast using K-means
PVset_Kmeans_Forecast
Forecast using LSTM
PVset_LSTM_Forecast
PV_err_distribution.mat
PV_pso_coeff.mat
1
2
3
4
5
6

## Slide 4
PVset_ANN_Train
Longterm data
Set Past data
Calculate correlation
Set feature column
Train Solar Forecast model (ANN)
Train Generation
Forecast model(ANN)
Save Forecast model
(.mat file)
Delete last 7days data
Delete row which has 0 generation
Between feature & gerneration
Between feature & gerneration
Run 3 times
ANN model has big variance
Layer option: [20,20,20,15]
Experience best performance
Train function: Scaled conjugate gradient
It is faster because it uses GPU
PV_fitnet_ANN.mat
1
+time
Notes: 시작

## Slide 5
Data Standardization
Calculate correlation
Data Format change
K=k_min : k_max
(5 : 30)
Devide data
(70%/30%)
Train kmeans & baysian using 70%
Forecast using vaild data(30%)
Calculate err & set k-value which has best performance
PVset_kmeans_Train
Longterm data
2
Between feature & gerneration
Between feature & gerneration
K-means use Euclidean distance so standardization is important
PVset_Format_Change
days <=31
K=2
yes
no
Train kmeans & baysian
Train kmeans & baysian for solar (k=30)
Train again using optimal k-value
Save Forecast model
(.mat file)
PV_Model.mat
1:Building index
2:Date / Month (12.15~3.15=1(winter), 5.15~8.15=3(summer), else= 2)
3:Humidity / max value
4:wind speed / mean value
5:Temparature / max value
6:Cloud / mean value
7:Rain / mean value
8:SolarIrradiance / mean value
9~104:Generation / 1~96 row → 9~104 column
+month

## Slide 6
Set past data
Data Standardization
Calculate correlation
Set feature & target
Set train option
Train LSTM for solar
Set feature & target
Train LSTM for generation
Save Forecast model
(.mat file)
3
PVset_LSTM_Train
Longterm data
Use Only 7 days data because of LSTM’s train speed
Between feature & gerneration
Between feature & gerneration
+time
LSTM Layer
sequenceInputLayer
lstmLayer(100)
lstmLayer(50)
fullyConnectedLayer
regressionLayer
PV_LSTM.mat

## Slide 7
PVset_ANN_Forecast
Forecast data Shortterm data
Load .mat file
(PV_fitnet_ANN)
Set data
Forecast solar using ANN
Mean result of solar
Forecast Generation using ANN
Mean result of generation
Error Correction
Delete row which has 0 generation
Time= hour0.25quarter
Forecast 3 time
Find sunset,sunrise time
Export results
Find sunset,sunrise
row in data
Delete the value except between the sunrise and sunset times.
Error Correction 1
Error Correction 2
Load .mat file
Forecast Generation 3 times using shortterm
Mean result
Delete the value except between the sunrise and sunset times.
Calculate err rate & mean err rate
Compensate the result by the mean error
result1
result2

## Slide 8
PVset_kmeans_Forecast
Forecast data Shortterm data
Load .mat file
(PV_Model.mat)
Data standardization
Forecast solar using kmeans & baysian
patterning data
Forecast Generation using
Kmeans & baysian
3 times
Mean result of generation
Export result1
1:Building index
2:Date / Month (12.15~3.15=1(winter), 5.15~8.15=3(summer), else= 2)
3:Humidity / max value
4:wind speed / mean value
5:Temparature / max value
6:Cloud / mean value
7:Rain / mean value
8:SolarIrradiance / mean value
9~104:Generation / 1~96 row → 9~104 column
Export result2
Return to the original data format
Error correction
Load .mat file
(PV_Model.mat)
Standardize shortterm data & Format change
Forecast Generation using
Kmeans & baysian
3 times
Mean result of generation
Make 0 at night time & calculate mean error rate
Compensate the result by the mean error

## Slide 9
PVset_LSTM_Forecast
Forecast data Shortterm data
Load .mat file
(PV_LSTM.mat)
Data standardization
Forecast solar using LSTM
Forecast Generation using LSTM
Mean result of generation
Return to the original data format
Error Correction
Find sunset,sunrise time
Find sunset,sunrise
row in data
Delete the value except between the sunrise and sunset times.
Error Correction 1
result1
Error Correction 2
Load .mat file
Forecast Generation 3 times using shortterm
Mean result
Delete the value except between the sunrise and sunset times.
Calculate err rate & mean err rate
Compensate the result by the mean error
result2
Export results

## Slide 10
Pvget_getPVModel
Get File path &
Set parameter
.mat file check
Load .mat file
(PV_pso_coeff.mat
PV_err_distribution.mat)
Forecast PV generation using each model
Reflect coefficients in results
Get deterministic result & Generate Result File
Reflect distribution at result
Make the confidence interval
Draw graph
Calculate MAPE
PVget_Graph_desc
Train ANN
(PVget_ANN_Train)
Train Kmeans
(PVget_Kmeans_Train)
Train LSTM
(PVget_LSTM_Train)
abs(mean(
PVget_getCI
Sort data(30,96)
Select data with 95% size (upper)
Select data with
5% size (lower)
Make boundaries
Calculate time step
Find last time’s row
Chang x-axis to 0~24
Drawing graph of result
Forecast data Shortterm data